## Slide 1: Lecture 7– Dynamic Programming – an optimization technique
Chiao-Ting Li
Postdoctoral Research Fellow
Department of Mechanical Engineering, University of Michigan

## Slide 2: Outline
Bellman’s principle of optimality
Toy example 1: the Shortest path problem
Toy example 2: SISO system
A realistic example: Prius 2010

## Slide 3: Dynamic Programming (DP)
The DP technique is based on the Bellman’s principle of optimality—“An optimal policy has the property that, whatever the initial state and optimal first decision may be, the remaining decisions constitute an optimal policy with regard to the state resulting from the first decision”*
DP is a recursive method for finding the optimal trajectory over a fixed horizon
DP solves the problem backwards in time, i.e., the solution starts when there is only one stage left in the decision process, and then move backwards recursively
*R. E. Bellman, Dynamic Programming. New Jersey: Princeton University Press, 1957.

## Slide 4: Shortest Path Problem
Goal: To find the shortest path from Node 1 to Node 8
1
2
3
5
4
6
7
8
Stage 0
Stage 1
Stage 2
Stage 3
2
3
4
5
4
6
1
2
3
2
4
1
5
3
4

## Slide 5: Shortest Path Problem
1
2
3
5
4
6
7
8
Stage 0
Stage 1
Stage 2
Stage 3
2
3
4
5
4
6
1
2
3
2
4
1
5
3
4
fi = shortest path from Node i to the end
tij = transitional cost from Node i to Node j
We will solve fi from the last stage
E. V. Denardo, Dynamic Programming: Models and Applications. New York: Prentice-Hall, 1982.

## Slide 6: Shortest Path Problem
1
2
3
5
4
6
7
8
Stage 0
Stage 1
Stage 2
Stage 3
2
4
5
6
1
3
2
4
Stage 3: (state from the end)
Stage 2:
Stage 1:
Stage 0:
5
3
4
4
2
1
3
The shortest path: 1  3  6 8
The shortest path length: 8

## Slide 7: Important Facts
To solve the overall optimization problem (from Node 1 to Node 8), we solved all the sub-problems (from all nodes to the terminal node)
Hence, DP is computationally expensive
DP problem was solved backwards in time
Principle of Optimality!!

## Slide 8: Dynamic Programming Algorithm
Step N:
Step k, for 0 ≤ k < N:
Found via interpolation
A Sequence of Simpler Problems
Terminal Cost
Cost-to-Go Function
The original optimization problem
Minimize the cost function
Subject to
Terminal Cost
Transitional Cost
System Dynamics
State Constraints
Control Constraints

## Slide 9: Single-Input, Single-Output Rotational Mechanical System
Input: external torque τ(t)
Output: angular displacement θ(t)
System Dynamics:
State-Space Description:
Parameters:
shaft inertia J
damping coefficient b
torsional spring constant kR
R. L. Williams and D. A. Lawrence, Linear state-space control systems: John Wiley & Sons, 2007.

## Slide 10: State Feedback Controller Design
Pole Placement
%% desired closed-loop dynamics
PO = 3; % overshoot percentage
ts = 0.7; % settling time [sec]
term = pi^2 + log(PO/100)^2;
zeta = log(PO/100)/sqrt(term); % damping ratio
wn = 4/(zeta*ts); % natural frequency
%% generic second-order frequency
num2 = wn^2; % numerator
den2 = [1 2*zeta*wn wn^2]; % denominator
CL_sys_pole = roots(den2); % desired eigenvalues
%% pole placement
K = place(A,B,CL_sys_pole)
K =
18.8627 7.4286
%% open-loop state-space realization
%% two states: x1: theta, x2: theta dot
J = 1; b = 4; kR = 40;
A = [0 1;
-kR/J -b/J];
B = [0;
1/J];
C = [1 0];
D = 0;
LQR Design
%% LQR design
Q = 20*eye(2);
R = 1;
KLQR = lqr(A,B,Q,R)
KLQR =
0.2492 2.0414

## Slide 11: Dynamic Programming
Use DP to solve the following problem:
with
Demonstrate how to implement DP numerically
  Calculate the cost-to-go function via interpolation
Compare DP solution with LQR solution to showcase that DP does produce optimal solutions
%% discrete-time system
[Ad, Bd] = c2d(A, B, Ts);
and

## Slide 12: Dynamic Programming Implementation
Quantize state values into finite grids:
(1,0)
(-1,0)
(0,1)
(0,-1)
x1_grid = -1:0.5:1;
x2_grid = -1:0.5:1;
(These are only examples. They are too coarse to be used in real implementation)

## Slide 13: Dynamic Programming Implementation
k = N
k = N-1
Two particular time steps:

## Slide 14: Dynamic Programming Implementation
k = N
k = N-1
Step N:
Calculate the terminal cost

## Slide 15: Dynamic Programming Implementation
Step N-1:
u_grid = -1:0.2:3;
Quantize control values into finite grids
xk = (0,0)
k = N
k = N-1
uk = 0
xk+1 = (0,0)
Calculate the cost-to-go function

## Slide 16: Dynamic Programming Implementation
xk = (0,0)
u_grid = -1:0.2:3;
Step N-1:
Another control value:
uk = 0.4
xk+1 = (0,0.4)
In general, xk+1 will not land “on the grid”
Therefore, interpolation is needed to find
Found via interpolation (MATLAB command: interp2)
k = N
k = N-1
Calculate the cost-to-go function

## Slide 17: Dynamic Programming Implementation
xk = (0,0)
Cost-to-go is found by searching through all possible control values
u_grid = -1:0.2:3;
Step N-1:
k = N
k = N-1

## Slide 18: Dynamic Programming Implementation
k = N
k = N-1
xk = (0.5,0)
Step N-1:
u_grid = -1:0.2:3;
x1_grid = -1:0.5:1;
x2_grid = -1:0.5:1;
Cost-to-go function is calculated for all state grids at Step N-1

## Slide 19: Dynamic Programming Algorithm
State and control values are quantized into finite grids
Solve recursive equation backwards in time
Step N:
Step k, for 0 ≤ k < N:
Obtain an optimal, time-varying, state-feedback control policy
 Stored in a table for each of the quantized states and time stages
DP creates a family of optimal paths for all possible initial conditions

## Slide 20: MATLAB Script
Ts = 0.05; % sampling time [sec]
n = 0:1:(4/Ts);
N = length(n);
x1_grid = -0.2:0.025:0.425;
x2_grid = -2:0.1:1;
u_grid = -1:0.2:3; % [1]x[21] vector
%% ==============================
%% step 1: transitional cost
L_table = zeros(length(x1_grid), length(x2_grid), length(u_grid), N);
x1n_table = zeros(length(x1_grid), length(x2_grid), length(u_grid), N);
x2n_table = zeros(length(x1_grid), length(x2_grid), length(u_grid), N);
for k = 1:N % loop for time
for i = 1:length(x1_grid) % loop for x1
x1 = x1_grid(i);
for j = 1:length(x2_grid) % loop for x2
x2 = x2_grid(j);
xn = repmat(Ad*[x1;x2],1,length(u_grid)) + Bd*u_grid;
x1n_table(i,j,:,k) = xn(1,:);
x2n_table(i,j,:,k) = xn(2,:);
L_table(i,j,:,k) = [x1;x2]'*Q*[x1;x2] + R*u_grid.^2;
end % end of loop for x2
end % end of loop for x1
end % end of loop for time
%% ==============================
%% step 2: cost-to-go
J_star = zeros(length(x1_grid), length(x2_grid), N);
u_opt = zeros(length(x1_grid), length(x2_grid), N);
k = N;
[X2,X1] = meshgrid(x2_grid, x1_grid);
J_star(:,:,k) = Q(1,1)*X1.^2 + Q(2,2)*X2.^2; % terminal cost
for k = N-1:-1:1 % backward loop for time
for i = 1:length(x1_grid) % loop for x1
for j = 1:length(x2_grid) % loop for x2
x1n = squeeze(x1n_table(i,j,:,k));
x2n = squeeze(x2n_table(i,j,:,k));
x1n(x1n>max(x1_grid)) = max(x1_grid);
x1n(x1n<min(x1_grid)) = min(x1_grid);
x2n(x2n>max(x2_grid)) = max(x2_grid);
x2n(x2n<min(x2_grid)) = min(x2_grid);
J_temp = squeeze(L_table(i,j,:,k)) + ...
interp2(x2_grid, x1_grid, J_star(:,:,k+1), x2n, x1n);
[opt_value, opt_id] = min(J_temp);
J_star(i,j,k) = opt_value;
u_opt(i,j,k) = u_grid(opt_id);
end
end
end
Parallelization (calculate xk+1 with all possible u at once)
Find via interpolation
Element-wise manipulation
%% ==============================
%% step 3: retrieve optimal solution
u_sim = zeros(1, N);
x1_sim = zeros(1, N);
x2_sim = zeros(1, N);
x0 = [0.4;
0.2];
x1_sim(1) = x0(1);
x2_sim(1) = x0(2);
for k = 1:N-1
u_sim(k) = interp2(x2_grid, x1_grid, u_opt(:,:,k), x2_sim(k), x1_sim(k));
xn = Ad*[x1_sim(k);x2_sim(k)] + Bd*u_sim(k);
x1_sim(k+1) = xn(1);
x2_sim(k+1) = xn(2);
end
Notes: 85 lines in total

## Slide 21: The Optimal Solution
Zoom In

## Slide 22: Computation Time
Pole Placement | LQR | Discrete LQR | Dynamic Programming
0.061 | 0.12 | 0.063 | 56.21
* Time in seconds

## Slide 23: Comments
DP is not (typically) real-time implementable
  computationally expensive; the “curse of dimensionality”
  needs future information, so that the problem can be solved backward in time
However, DP can
  handle non-linearity, constraints, discontinuity
  guarantee global optimality over a horizon
  provide benchmarking performance

## Slide 24: HEV Problem Formulation
Control Inputs
  Te: engine torque
  Tm: motor torque
Minimize the cost function
Constraints
Discrete-time nonlinear system
State variables
  ωe: engine speed
  SOC: battery state of charge

## Slide 25: Prius 2010
* N. Kim, A. Rousseau and E. Rask, "Vehicle-level control analysis of 2010 Toyota Prius based on test data," Proceedings of the Institution of Mechanical Engineers, Part D: Journal of Automobile Engineering, vol. 226, pp. 1483-1494, 2012.

## Slide 26: Prius 2010
Goal: To optimize fuel consumption over a predefined driving cycle

## Slide 27: Prius 2010
The assumption to simplify the problem:
Original Problem
Controls:
States:
u1: engine torque
u2: MG1 torque
x1: engine speed
x2: battery state of charge
Simplified Problem
Control:
States:
u: MG1 torque
x1: engine speed
x2: battery state of charge
Assumption:
Engine operates along the optimal BSFC line
Problem dimension: 4
Problem dimension: 3
Goal: To optimize fuel consumption over a predefined driving cycle

## Slide 28: MATLAB Script
Step 1: calculate transitional cost L(xk,uk)
Step 2: calculate cost-to-go function
Step 3: retrieve optimal control & solution trajectories

## Slide 29: Numerical Treatment to Enforce Constraints
  the batter way: apply finite but sufficiently high penalty on x2 (battery SOC) to prevent over discharge
Soft constraints
  the no-brainer way: apply Inf to grids that have constraint violation
  However, MATLAB cannot perform interpolation on tables with Inf or nan
Hard constraints

## Slide 30: Truncated NEDC Cycle
Engine is used less often
(Engine is never used if the SOC starts above 0.48)
Different SOC initial conditions

## Slide 31: Truncated NEDC Cycle
More expensive penalty on final SOC (larger α)
Batter SOC regulation

## Slide 32: Full NEDC Cycle
Different SOC initial conditions

## Slide 33: Fuel Economy
The fuel consumption needs to be corrected to rule out the SOC effect, so that the fuel economy can be compared fairly
Use cftool in MATLAB or “Add Trendline” in Excel to perform a linear curve fit

## Slide 34: Fuel Economy in Different Driving Cycles

## Slide 35: Homework
A toy HEV problem:
  with discrete-time dynamics:
where
xk is the state at time k (SOC),
uk is the control signal at time k (engine power),
wk is the disturbance signal at time k (power demand)
N is the problem horizon,
The driving cycle is assumed to be know and has the following power demand profile:
(The coarse grids are selected so that the optimization problem can be solved manually)

## Slide 36: Homework
Goal: find optimal control policy to minimize the cost function
Use the following values:

## Slide 37: Homework
Step N:
Step k, for 0 ≤ k < N: